## Slide 1: Fixed Point FIR Filter Implementation with Arduino Uno

## Slide 2: Steps for Filter Implementation
Filter Specifications
Finding filter coefficients
Getting the input signal
Do convolution to get output signal

## Slide 3: Filter Specifications
Low-pass FIR type-1 filter
Sampling frquency (fs) = 2000Hz
Cutoff frquency (fc) = 100Hz
Order = 32
No. of coefficients = Order +1

## Slide 4: Finding filter coefficients
MATLAB fir filter design
MATLAB command:
h = fir1(M, fc / fs)
Fixed-point conversion
8 bit, 1 bit for signed integer & 7 bits for fraction
MATLAB command:
h_fixed=fi(h, 1, 8, 7)

## Slide 5: Getting the input signal
Sampling frquency (fs) = 2000Hz
f1 = 50Hz
f2 = 500Hz
Signal = sin(2*pi*f1*t)+sin(2*pi*f2*t)

## Slide 6: Do convolution to get output signal
MATLAB command:
h = conv(sig_fixed,h_fixed)
In Arduino IDE,
Store input signal and filter coefficients
Then write Arduino code for convolution
Input signal length = 500
Filter length =33
Output signal length = 500+33-1 = 532